TELEPHONY MENU
## The "Telephony" menu
The Wireshark Telephony menu contains the fields shown in table.
All menu items will bring up a new window showing specific telephony related statistical information.

Table. Telephony menu items
Menu Item		Description
IAX2		Inter-Asterisk eXchange v2 (IAX2) / VoIP protocol developed primarily for communication between Asterisk servers. / Protocol dependencies: IAX2 uses UDP as its transport protocol. The well known UDP port for IAX2 traffic is 4569. / The IAX2 dissector is fully functional for non-trunked packets. Separate calls are identified and tracked, and provided the start of a call is captured, the payload is passed to subdissectors. Recent versions of wireshark also include logic to calculate how "late" a packet is relative to its timestamp. Trunked packets show only their type (3 - meta packet).
SMPP Operations...		Short Message Peer to Peer (SMPP) / This protocol is specifically targetted at transferring Short Messages between a Short Message Service Centre (SMSC) and an application using transport like TCP or X.25. With this you can thus, using plain TCP, indirectly submit Short Messages to a mobile (cell phone) or receive from them. / SMPP uses TCP as its transport protocol (though it is no stranger to X.25 as well). No well known port is defined for this protocol. The dissector will use heuristics to determine from the fixed header whether the captured packet is SMPP or not.
SCTP		Stream Control Transmission Protocol (SCTP) / Transport Protocol for call signalling, created to overcome several lacks and problems of TCP when used for signalling between telephony nodes. / SCTP uses IP as its underlying protocol. The assigned protocol number for SCTP on IP is 132. / Three preference settings exist for SCTP: / Checksum type / If Control chunks should be shown or not / If Heuristic sub-dissectors should be shown first / If the wrong checksum type is selected, the checksum might show up as incorrect.
ANSI		American National Standards Institute (ANSI) / ANSI facilitates the development of American National Standards (ANS) by accrediting the procedures of standards developing organizations (SDOs). These groups work cooperatively to develop voluntary national consensus standards. Accreditation by ANSI signifies that the procedures used by the standards body in connection with the development of American National Standards meet the Institutes essential requirements for openness, balance, consensus and due process.
GSM		Global System for Mobile communication (GSM) protocol family / GSM is a technology for digital wireless telecommunications, represented by a decent number of specifications. Parts of GSM are based on the fixed-line ISDN technology. / The original "air interface" for GSM handsets, for second-generation (2G) wireless telephony, was a TDMA interface; the third-generation interface, W-CDMA, is a CDMA interface. GSM, however, refers to more than just the "air interface"; it refers to the complete set of protocols.
H.225...		H.225 "Call signalling protocols and media stream packetization for packet-based multimedia communication systems" is a VoIP protocol. / H.225 is independent of the underlying transport protocol.
ISUP Messages...		ISDN User Part (ISUP) / This protocol is used as signalling in trunks between telephone exchanges to establish and release calls. / ISUP is standardized by ITU-T in Q.761 to Q.769. There are several national variants as well. .
LTE		LTE MAC Traffic Statistics / It shows statistics of the captured LTE MAC traffic.
MTP3		Message Transfer Part Level 3 (MTP3) / MTP3 is part of the SS7 stack. It is NOT part of the SIGTRAN family of protocols. The purpose of the SIGTRAN family of protocols is to carry SS7 traffic over IP networks. / The hardware and software functions of the SS7 protocols are divided into functional abstractions called "levels". These levels map loosely to the Open Systems Interconnect (OSI) 7-layer model defined by the International Standards Organization (ISO). / Different MTP3 flavors exist: / ANSI T1.111.4-1996 / ITU-T Q.704 7/1996 / GF 001-9001 (Chinese ITU variant) / The MTP3 dissector is fully functional. It supports standard ITU MTP3 as well as the ANSI, Chinese, and Japanese variants (the variant selection is a Preference of the dissector). Some national options (such as congestion levels) are supported via preference settings. / Wireshark also contains an "MTP3MG" ("MTP3 Management") dissector for MTP3 control messages. These are messages exchanged between the MTP3 layer management at each endpoint.
RTP		The RTP analysis function takes the selected RTP stream (and the reverse stream, if possible) and generates a list of statistics on it. / Starting with basic data as packet number and sequence number, further statistics are created based on arrival time, delay, jitter, packet size, etc. / Besides the per packet statistics, the lower pane shows the overall statistics, with minimums and maximums for delta, jitter and clock skew. Also an indication of lost packets is included. / The RTP Stream Analysis window further provides the option to save the RTP payload (as raw data or, if in a PCM encoding, in an Audio file). Other options a to export and plot various statistics on the RTP streams.
SIP...		Session Initiation Protocol (SIP) / The Session Initiation Protocol (SIP) is an application-layer control (signaling) protocol for sessions. / These sessions include Internet telephone calls, multimedia distribution, and multimedia conferences. SIP can create, modify, and terminate sessions with one or more participants. / The SIP protocol is a member of the VOIPProtocolFamily.
UCP Messages...		Universal Computer Protocol (UCP) / This protocol is specifically targetted at transferring Short Messages between a Short Message Service Centre (SMSC) and an application using transport like TCP or X.25. / With this you can thus, using plain TCP, indirectly submit Short Messages to a mobile (cell phone) or receive from them. / UCP uses TCP as its transport protocol. No well known port is defined for this protocol. The dissector will use heuristics to determine from the packet(s) whether the captured data is UCP or not. WSP: The WAP protocol stack can use short messages as a bearer.
VoIP Calls...		The VoIP Calls window shows a list of all detected VoIP calls in the captured traffic. It finds calls by their signaling. / To access the VoIP calls analysis use the menu entry "Telephony->VoIP Calls...". The current VoIP supported protocols are: / SIP / H323 / ISUP / MGCP / UNISTIM / with the corresponding RTP streams. / The VoIP calls list shows the following information per call: / Start Time: Start time of the call. / Stop Time: Stop time of the call. / Initial Speaker: The IP source of the packet that initiated the call. / From: For H323 and ISUP calls, this is the calling number. For SIP calls, it is the "From" field of the INVITE. For MGCP calls, the EndpointID or calling number. For UNISTIM the Terminal ID. / To: For H323 and ISUP calls, this is the called number. For SIP calls, it is the "To" field of the INVITE. For MGCP calls, the EndpointID or dialed number. For UNISTIM the dialed number. / Protocol: Any of the protocols listed above / Packets: Number of packets involved in the call. / State: The current call state. The possible values are / CALL SETUP: call in setup state (Setup, Proceeding, Progress or Alerting) / RINGING: call ringing (only supported for MGCP calls) / IN CALL: call is still connected / CANCELLED: call was released before connect from the originated caller / COMPLETED: call was connected and then released / REJECTED: call was released before connect by the destination side / UNKNOWN: call in unknown state
WAP-WSP...		The Wireless Application Protocol (WAP) consists of a set of protocols that allow the deployment of Internet-like services on a lot of wireless network technologies. / Wireless Session Protocol (WSP) / The Wireless Session Protocol offers the HTTP request-response paradigm, and in addition it offers a new service named Wap Push, allowing applications in the network to push (unsolicited) data to a push-enabled application on the mobile device. / The Wireless Session Protocol started with the knowledge that many header names and values in the Hyper_Text_Transfer_Protocol are fixed strings. With efficient over-the-air usage of the bandwidth in mind, WSP attempts at encoding these fixed strings in a compact binary manner. This way, the header cache-control: no-cache can be encoded in 2 bytes: one for the header name (cache-control) and one for its value (no-cache). / There are 2 types of WSP: / Connectionless WSP (CL-WSP) only offers unreliable transport of WSP primitives, both pull (request and response) and push (single message). / Conection-oriented WSP (CO-WSP) offers the same services as CL-WSP, extended with connection (session) management, session capability negotiation, larger data transfer (segmentation and reassembly) and reliable data transport (acknowledgement mechanism).